## Slide 1
GridMind
AI and Blockchain Integration in Smart Grids for Autonomous Energy Trading and Risk Optimization
Taha Can Tilkioğlu · Serhat Yiğit · Cem Yılmaz
Engineering Management · Poznań University of Technology
Supervisor: Dr. Fredrick Mumali
Notes: Good morning. GridMind evaluates battery control, forecast value and settlement accounting. Our intended application is a Polish battery trader, while our completed measured experiments use six Irish households. I will keep these settings distinct. Sixty additional training runs and a forecast-to-control experiment show how design choices change outcomes. The evidence supports a reproducible evaluation, not a claim of validated Polish trading profit.
Evidence: results/extension/control_results.json; results/ablations/results.json; results/forecast_control/results.json. Polish components: src/gridmind_research/polish_market.py and docs/POLISH_MARKET_STUDY.md.

## Slide 2
Research objective and market role
Application target: a price-taking BESS trader in Poland
Completed measured study: six Irish households under assumed tariffs
Community outcome: net cost and the distribution of savings
Polish preparation: physical scheduling and forecast timing checks
Polish market profitability and a daily risk constraint remain untested.
2
Notes: The intended beneficiary is a price-taking battery trader or aggregator in Poland. Its proposed objective is net arbitrage value under physical and risk limits. The existing Irish demonstrator instead minimizes community cost under assumed tariffs. We cannot report its savings as Polish trading profits. We have implemented a separate aggregate scheduling baseline and strict time and forecast validation for the Polish design, but the market dataset and forecast-conditioned policy remain untested. This distinction is necessary for an honest application claim.
Evidence: results/extension/control_results.json; results/ablations/results.json; results/forecast_control/results.json. Polish components: src/gridmind_research/polish_market.py and docs/POLISH_MARKET_STUDY.md.
Market source: https://www.entsoe.eu/network_codes/cacm/implementation/sdac/

## Slide 3
Experiments and their connections
Experiment | Comparison | Evidence
Allocation | Proportional, welfare LP, Nash | Savings and fairness
Battery control | Control and forecast interventions | Cost, feasibility and household outcomes
Settlement | Solidity and signed SQLite | Balance parity and rejection checks
New intervention: causal forecasts feed the same MPC and change realized cost.
3
Notes: The allocation pilot measures distribution of benefits. Battery experiments measure intertemporal control cost. The settlement comparison replays an identical control-derived transaction stream in two ledgers. A new experiment now replaces the forecast entering the same MPC and measures downstream cost. Thus this forecast-control connection is implemented, while the learned actors still use their existing observations. Savings across experiments cannot be added because their outside options differ.
Evidence: results/extension/control_results.json; results/ablations/results.json; results/forecast_control/results.json. Polish components: src/gridmind_research/polish_market.py and docs/POLISH_MARKET_STUDY.md.

## Slide 4
Measured profiles and chronological evaluation
Data or split | Recorded coverage
Source | StoreNet Ireland, households H1–H6, 2020
Training | 404 complete four-hour episodes, January–April
Validation | 105 episodes, May
Evaluation | 44 episodes, 1–14 June
Retained test intervals | 704 of 1,344 intervals, 52.38%
Batteries and tariffs are assumptions. June dates had already been inspected in the allocation pilot.
4
Notes: Target duration: 50 seconds.
Consumption and photovoltaic production are measured StoreNet profiles. Battery capacities and prices are scenario assumptions. Each episode contains sixteen consecutive fifteen-minute intervals and a valid preceding measurement. Incomplete episodes are excluded without carrying battery state across gaps. Training uses January to April, checkpoint selection uses May, and evaluation uses early June. However, June had already been inspected in the first pilot. I therefore describe the result as exploratory chronological evaluation, rather than an untouched confirmatory test. The retained intervals are only about half of the possible period, so these totals are not complete electricity bills.
Turkish rehearsal cue: Gerçek veri ile varsayılan batarya ve tarifeyi ayır. Eksik veri oranını gizleme.
Evidence: gridmind/results/pilot_results.json and gridmind/results/extension/.
https://doi.org/10.1038/s41597-024-03454-2
https://doi.org/10.6084/m9.figshare.c.6829134

## Slide 5
Battery feasibility and causal observations
Constraint | Implementation
Capacity and power | 2 kWh nominal, 2 kW AC per household
Operating bounds | 0.2–1.8 kWh, 95% charge/discharge efficiency
Boundary condition | Every episode starts and finishes at 1 kWh
Available information | Previous net load, current SOC, clock and known tariff
Action protection | Power, SOC and terminal-reachability projection
Terminal restoration has a cost. No controller receives free energy at an episode reset.
5
Notes: Target duration: 50 seconds.
All controllers use the same physical battery model. A projection layer prevents power and state-of-charge violations and preserves the ability to reach the common terminal energy. The final restoration enters energy exchange and cost. This avoids rewarding a controller merely for emptying its battery at the end. Observations contain the preceding measured net load, rather than the current target or future demand. The model represents an unconstrained single bus. Energy conservation is verified, but voltage and thermal limits are not modelled.
Turkish rehearsal cue: SOC, terminal koşul ve veri sızıntısının engellenmesini açıklayabilmelisin.
Evidence: gridmind/results/pilot_results.json and gridmind/results/extension/.

## Slide 6
Learning comparison and training budget
Setting | IPPO | MAPPO
Actor at execution | Local, shared parameters | Local, shared parameters
Critic during training | Local observations | All household observations
Reward | Mean community incremental savings | Same reward
Random seeds | 11, 22, 33, 44, 55 | Same five seeds
Budget per seed | 11,520 joint steps | 11,520 joint steps
Original 60-update protocol. The follow-up varies actions, budget and reward.
6
Notes: The table describes the original ten learned policies. Actor architecture, five requested actions, shared economic reward and training budget match, while critic information differs. The follow-up crosses discrete and continuous actions with sixty and three hundred updates, retaining five seeds per algorithm. Another matched comparison adds a signed-benefit dispersion penalty using fourteen inputs in both arms. MPC still differs in information and decision procedure, so its comparison with the learned policies remains a comparison of complete controllers.
Evidence: results/extension/control_results.json; results/ablations/results.json; results/forecast_control/results.json. Polish components: src/gridmind_research/polish_market.py and docs/POLISH_MARKET_STUDY.md.

## Slide 7
Original control comparison at 60 updates
Chart: 
| Idle | Rule | MPC | IPPO | MAPPO
Cost EUR | 159.4083 | 171.1107 | 159.1604 | 173.3106 | 182.8197
EUR over the same 44 episodes. IPPO/MAPPO bars show five-seed means. Seed SD: 19.51 / 22.42 EUR.
7
Notes: This chart retains the original sixty-update comparison. Persistence MPC costs about 159.16 euros against 159.41 for idle sharing. IPPO averages 173.31 and MAPPO 182.82 euros. The new action and budget study narrows the explanation: all ten discrete policies at three hundred updates match idle behavior. That removes excess cycling cost but does not beat MPC. These results share previously inspected June data, so none is independent confirmation.
Evidence: results/extension/control_results.json; results/ablations/results.json; results/forecast_control/results.json. Polish components: src/gridmind_research/polish_market.py and docs/POLISH_MARKET_STUDY.md.

## Slide 8
Efficiency and fairness can rank policies differently
Allocation method | Savings EUR | Mean daily normalized Jain
Welfare LP | 26.0954 | 0.7741
Nash, 5% tolerance | 25.8716 | 0.8187
Proportional | 24.6755 | 0.8642
Heterogeneous-tariff allocation pilot. Its grid-only baseline differs from the battery experiment.
8
Notes: Target duration: 45 seconds.
In the separate allocation pilot, the Nash solution retains about 99.14 percent of welfare-LP savings and improves the reported Jain score relative to that LP. Yet proportional allocation has the higher Jain score in this comparison. A sophisticated objective therefore does not imply superiority under every fairness metric. Under homogeneous tariffs, total savings depend on matched energy volume, so policies matching the same volume have equal total savings. In the battery experiment, negative household benefits are preserved. Jain is left undefined when its chosen nonnegative-benefit interpretation fails.
Turkish rehearsal cue: Nash adaleti her yönteme göre artırdı deme. Karşılaştırmanın bazını ve metriğini söyle.
Evidence: gridmind/results/pilot_results.json and gridmind/results/extension/.

## Slide 9
Both ledgers reproduce the same 64 settlements
Measurement | Observed result
Final balances | Exact match across seven accounts
Total accounting credit | 6,000,000,000 micro-EUR units conserved
Solidity deployment | 641,807 gas
Settlement gas | 4,424,772 total, 68,917 median
Rejection and signature checks | 10 of 10 passed
Local PyEVM chain and Ed25519-signed SQLite. No real currency or public-chain performance claim.
9
Notes: Target duration: 50 seconds.
The first sixty-four positive trades from the fixed MAPPO seed eleven run were replayed in both systems. The same integer transaction inputs produced the same final balances and conserved all accounting credit. Checks include duplicate identifiers, unauthorized calls, insufficient funds, invalid trades, rollback and signature tampering. The Solidity contract was compiled and executed on a local EVM. This establishes accounting behavior in that environment. Both systems still trust an operator for metering. The experiment therefore does not demonstrate that blockchain is commercially necessary or that its consensus performs well on a public network.
Turkish rehearsal cue: Akıllı sözleşme gerçekten çalıştı; fakat yerel zincir, gerçek para ve dağıtık konsensüs testi değil.
Evidence: gridmind/results/pilot_results.json and gridmind/results/extension/.
https://docs.soliditylang.org/en/v0.8.30/
https://ethereum.org/developers/docs/smart-contracts/testing/

## Slide 10
Verification and evidence limits
37 research tests cover physical, causal and data boundaries
70 saved checkpoints include 60 controlled follow-up runs
Maximum energy-balance residual remains below 1.4 × 10⁻¹⁵ kWh
Later evaluation adds 501 episodes across 168 days in the same six homes
No enforced daily CVaR constraint, feeder validation or demonstrated annual return on investment.
10
Notes: Sources: results/revision_20260928_tests.log and results/later_period_verification.json. The 37 research tests pass. The later-period audit covers 65 arms and 195390 household-episode rows. Maximum absolute energy residual is 1.3322676295501878e-15 kWh and terminal residual is zero. These are model consistency checks, not physical feeder or market validation. The same six households and documented prior access limit inference.

## Slide 11
June follow-up findings
Discrete actions at 300 updates reproduce idle cost in all 10 runs
The fixed fairness penalty gives no consistent improvement
Ridge MPC costs 158.8618 EUR, with losses for two households
First-step forecast accuracy and control value rank differently
June remains exploratory. Backups G and H report the later temporal evaluation.
11
Notes: The controlled experiments supply three useful findings. First, increasing the discrete-policy budget to three hundred updates reproduces idle cost in all ten runs. Second, continuous actions do not establish an advantage and the fixed fairness penalty does not consistently improve distribution. Third, Ridge forecasts fed into the same MPC reduce total cost to 158.8618 euros. First-step MAE is slightly worse, but horizon MAE is lower. Two households still lose relative to idle. Prediction accuracy, total saving and individual benefit must therefore be evaluated separately.
Evidence: results/extension/control_results.json; results/ablations/results.json; results/forecast_control/results.json. Polish components: src/gridmind_research/polish_market.py and docs/POLISH_MARKET_STUDY.md.

## Slide 12
Conclusion
The prototype connects causal forecasts, MPC and physical accounting
Learning variants show no aggregate cost advantage over MPC
Community gains and correct ledgers do not guarantee individual benefit
Later profiles extend the evidence. Independent confirmation remains open
Questions
12
Notes: The July-December extension evaluates 501 episodes on 168 retained days. Ridge MPC costs 1939.3432 EUR, persistence 1946.6754 EUR and idle 1947.4997 EUR. All discrete 300-update policies reproduce idle again. The protocol discloses prior partial access, so this is exploratory temporal evidence. Polish market validation remains pending. Source: results/later_period/results.json and family_summary.csv. ChatGPT/Codex assisted preparation; see thesis Section 1.3.

## Slide 13
Backup A Original controller results
Controller | Mean cost EUR | Seed SD EUR | Saving vs idle EUR
Idle | 159.4083 | n/a | 0.0000
Rule | 171.1107 | n/a | −11.7024
MPC | 159.1604 | n/a | 0.2478
IPPO | 173.3106 | 19.5128 | −13.9023
MAPPO | 182.8197 | 22.4156 | −23.4114
SD describes variation among five training seeds, not independent households or days.
13
Notes: Backup slide. These are the original sixty-update controller results. The sixty-run follow-up is in results/ablations, and the four forecast substitutions are in results/forecast_control. Seed standard deviation describes training variability, not uncertainty across independent households or dates.
Evidence: results/extension/control_results.json; results/ablations/results.json; results/forecast_control/results.json. Polish components: src/gridmind_research/polish_market.py and docs/POLISH_MARKET_STUDY.md.

## Slide 14
Backup B Forecasts change MPC cost
Chart: 
| Persistence | Previous day | Ridge | Oracle*
Total community cost EUR | 159.1604 | 160.3051 | 158.8618 | 153.7614
EUR over the same 44 episodes. Oracle uses future measurements and is non-causal.
14
Notes: Backup slide. The same MPC uses four different net-load forecasts on forty-four episodes. Costs are 159.1604 euros for persistence, 160.3051 for previous-day, 158.8618 for Ridge and 153.7614 for perfect information. The oracle reads future measurements and is not deployable. Ridge first-step MAE is 0.08424 kWh versus 0.08295 for persistence, while horizon MAE improves from 0.14948 to 0.12770. The original aggregate forecasting pilot uses a different target and sample.
Evidence: results/extension/control_results.json; results/ablations/results.json; results/forecast_control/results.json. Polish components: src/gridmind_research/polish_market.py and docs/POLISH_MARKET_STUDY.md.

## Slide 15
Backup C Tariffs and economic boundary
Scenario input | Assumed value
Import before 07:00 | 0.20 EUR/kWh
Import 16:00–20:00 | 0.42 EUR/kWh
Other import periods | 0.30 EUR/kWh
Export and local fee | 0.08 and 0.02 EUR/kWh
Battery throughput cost | 0.01 EUR per AC kWh
Historical measured profiles replay under scenario tariffs. No observed retail bill or market-price join.
15
Notes: Backup slide.
These are assumptions for the battery experiment, common across households. They are not current Polish or Irish tariffs. The time labels remain in the source clock because an external time-zone join was not verified.
Turkish rehearsal cue: Birimleri karıştırma: kW güç, kWh enerji, EUR/kWh birim fiyat.
Evidence: gridmind/results/pilot_results.json and gridmind/results/extension/.

## Slide 16
Backup D June risk and household outcomes
CVaR95 averages the worst 5% of episode costs
44 episodes provide only 2.2 tail episode-equivalents
Ridge MPC saves in total while H1 and H5 lose relative to idle
A community saving does not establish individual rationality
No daily risk budget or learned fairness guarantee is enforced.
16
Notes: Backup slide. CVaR95 uses fractional-tail weighting and forty-four episodes supply only 2.2 tail-episode equivalents. Under persistence MPC, H1 loses about 0.0257 euros. Under Ridge MPC, H1 loses 0.0578 and H5 loses 0.0138 euros. The fairness penalty was tested, but no participation guarantee or daily risk constraint has been established.
Evidence: results/extension/control_results.json; results/ablations/results.json; results/forecast_control/results.json. Polish components: src/gridmind_research/polish_market.py and docs/POLISH_MARKET_STUDY.md.

## Slide 17
Backup E Evidence and demo route
Open the offline results viewer for controller and household outcomes
Inspect the 60-run ablation and four-arm forecast results
Use both original and follow-up evidence verification scripts
Saved-policy replay matches the recorded follow-up costs
The offline viewer displays recorded results. A fresh evaluation is a separate command.
17
Notes: Backup slide. The offline viewer retains the original controller results. Current follow-up data are in results/ablations and results/forecast_control. verify_defense_evidence.py audits the archive and original records. verify_follow_up.py checks the sixty-run and forecast-coupling records. Both read saved evidence; neither starts training. The full commands and required dependencies are in docs/ABLATION_REPRODUCTION.md.
Evidence: results/extension/control_results.json; results/ablations/results.json; results/forecast_control/results.json. Polish components: src/gridmind_research/polish_market.py and docs/POLISH_MARKET_STUDY.md.

## Slide 18
Backup F Selected primary sources
Trivedi et al. (2024), StoreNet community dataset
Yu et al. (2021/2022), PPO in cooperative multi-agent games
Jain et al. (1984), resource-allocation fairness
Rockafellar and Uryasev (2000), conditional value at risk
Wüst and Gervais (2018), blockchain trust-model decision
Complete references and links appear in the manuscript and speaker notes.
18
Notes: Backup slide.
Dataset: https://doi.org/10.1038/s41597-024-03454-2
MAPPO: https://arxiv.org/abs/2103.01955
Jain: https://arxiv.org/abs/cs/9809099
CVaR: https://sites.math.washington.edu/~rtr/papers/rtr179-CVaR1.pdf
Blockchain: https://eprint.iacr.org/2017/375
Turkish rehearsal cue: Kaynakları ezberlemek yerine hangi kararını desteklediklerini öğren.
Evidence: gridmind/results/pilot_results.json and gridmind/results/extension/.

## Slide 19
Backup G Later period outcomes
19
Controller | Cost EUR | Saving vs idle EUR
Idle sharing | 1947.4997 | 0.0000
Self-consumption rule | 2065.3425 | −117.8428
Persistence MPC | 1946.6754 | 0.8243
Previous-day MPC | 1966.2359 | −18.7361
Ridge MPC | 1939.3432 | 8.1565
Discrete IPPO 300, five-seed mean | 1947.4997 | 0.0000
501 common episodes, July–December 2020. Frozen models, scenario tariffs.
Notes: Source: results/later_period/family_summary.csv. Measured StoreNet profiles, six households, fixed scenario tariffs and batteries. All costs refer only to retained four-hour episodes, not complete annual bills. Sixty policies and five baselines were evaluated; no retraining. Primary discrete IPPO minus persistence difference +0.824335 EUR. Prior partial access is documented in configs/later_period_protocol.json.

## Slide 20
Backup H Coverage and uncertainty
20
501 episodes across 168 days cover 45.38% of candidate blocks
Only 1 midnight and 11 morning blocks starting at 04:00 remain
Ridge minus persistence: −0.04364 EUR per retained source day
95% seven-day block interval: [−0.06889, −0.02127] EUR per day
Conditional exploratory inference. Prior access and incomplete coverage limit the claim.
Notes: Sources: results/later_period/results.json, eligibility.csv and hour_coverage.csv. 10000 circular moving-block draws, seed 25092026. Blocks follow eligible days; gaps mean seven eligible days are not always seven calendar days. Ridge has lower daily cost on 60 days, ties on 54 and higher cost on 54. Its total advantage over persistence is 7.332171 EUR, approximately 0.38%. The primary discrete-IPPO contrast has seven-day interval [-0.0000797283,0.0111102746] EUR/day, including zero. Neither equivalence nor population-level superiority is established.